## Slide 1
EE 446 · TINYML FOR ULTRA LOW-POWER EDGE COMPUTING · SPRING 2026
Golf Swing Sound Classification
on the Edge
A TinyML audio classifier that tells a clean strike from a fat (ground) or topped shot — running entirely on an Arduino Nano 33 BLE Sense.
Team: [Golf Swing Classification] • Kenzie · Mihir · Sparsh
Notes: Title. One-sentence hook: we classify the sound of a golf swing into good/ground/top, fully on a microcontroller. Replace the team placeholders before presenting.

## Slide 2
Problem & Motivation
Why golf-swing audio, and why TinyML
Golfers get almost no objective feedback on contact quality.
But the sound of impact carries it — a clean strike, a fat “ground” hit, and a thin “topped” shot each have a distinct acoustic signature. We classify that sound in real time.
Why TinyML fits: always-on and battery-powered, mounts on the club or bag, gives instant feedback with no phone or cloud, keeps data private, and runs on ~$30 of hardware.
Success criteria: classify each swing in real time on the board itself — no phone or cloud — within the Nano's 256 KB RAM / 1 MB flash, at or above baseline accuracy.
G
GOOD
Clean strike — sharp, balanced transient
G
GROUND
Fat hit — low-frequency thump
T
TOP
Topped shot — thin, bright “tink”
Notes: Problem. Golfers lack objective contact feedback; the impact sound encodes it. TinyML lets it be always-on, private, cheap, no phone/cloud. Name the three shot types and their sounds.

## Slide 3
Task, Data & Metrics
3-class audio classification on self-collected data
TASK
3-class audio classification: Good / Ground / Top
SENSOR & INPUT
Onboard PDM microphone — recorded at 48 kHz, resampled to 16 kHz for the model
DATASET
~76 real swing recordings (≈4 min): Good 28 · Ground 24 · Top 24, expanded with a custom augmentation pipeline
SPLIT & PREPROCESSING
80 / 20 train-test — augmented data in the training set only (no leakage). 500 ms window, 250 ms stride, MFE (40 mel bands).
EVALUATION METRICS
Accuracy
overall + held-out test
Per-class F1
Good / Ground / Top
AUC (ROC)
ranking quality
Confusion matrix
where errors fall
Plus on-device cost: latency, RAM, and Flash footprint.
Notes: Data. 3 classes, onboard mic at 48k resampled to 16k, ~76 real clips expanded by augmentation. Stress the 80/20 split with augmented data in training ONLY - that is why our test number is honest.

## Slide 4
System Overview
End-to-end pipeline: sound in → class out
PDM Mic
16 kHz audio
→
Windowing
500 ms / 250 ms
→
MFE
40 mel bands
→
1D CNN
int8 classifier
→
Output
Good / Ground / Top
All five stages run on-device on the Arduino Nano 33 BLE Sense — nothing leaves the board.
Notes: System overview. Walk left to right: mic, windowing, MFE features, 1D CNN, output - all on-device. 30 seconds, keep it moving.

## Slide 5
Baseline ML Model
Full-precision Keras model trained in Edge Impulse
ARCHITECTURE
Input — MFE features (1,960)
Reshape — 40 columns
1D Conv / Pool — 8 filters
Dropout 0.25
1D Conv / Pool — 16 filters
Dropout 0.25
Flatten → Dense (3 classes)
88.8%
validation accuracy · 74.5% held-out test (float32)
Why this model
A compact 1D-CNN over MFE spectrogram features — well suited to short, transient impact sounds and small enough to compress for the target board.
Trained 100 cycles, learning rate 0.005, with audio data augmentation enabled.
Notes: Baseline model. Compact 1D-CNN over MFE features. 88.8% validation in full precision. Mention it is small by design so it survives quantization.

## Slide 6
TinyML Deployment Pipeline
From float32 Keras to a flashed Arduino library
1
MFE DSP
block
→
2
float32
Keras model
→
3
int8 PTQ
quantization
→
4
TFLite
Micro
→
5
EON
Compiler
→
6
Arduino
library → flash
127 ms
inference latency
(per window)
11.8 KB
peak RAM used
(of 256 KB)
75.9 KB
Flash used
(of 1 MB)
Notes: TinyML pipeline. The deployment path for the final model (Impulse 3): int8 PTQ, TFLite Micro, EON Compiler, Arduino library, flash. Fits the board easily: 11.8 KB RAM of 256 KB, 75.9 KB flash of 1 MB.

## Slide 7
Advanced Component: Augmentation Ablation
Custom data-augmentation pipeline + a controlled ablation study
1
REJECTED
Aggressive augmentation
Shift + noise + gain + time-stretch + pitch. Stretching 0.16 s transients mangled the Top class → overfit, poor generalization.
2
KEPT
Gentle augmentation
Shift + light noise only. Cleaner transients → higher AUC, fewer hard errors. Carried into the final model.
3
REJECTED
EON MFE autotune
Auto-picked DSP params. Validation fell ~89% → 69% and smeared the strong classes → reverted to defaults.
Key insight: augmentation must respect the signal — gentle transforms generalized, aggressive ones destroyed short impacts. A 0.5 confidence threshold then gave the honest, comparable test numbers used to pick the final model.
Notes: Advanced component - this is the graded one. We built a custom augmentation pipeline and ran an ablation: aggressive aug overfit and wrecked Top; gentle aug generalized; EON autotune backfired and we reverted. Threshold tuning took test accuracy 61 -> 74.5%.

## Slide 8
Tiny Model Results
Baseline vs. deployed model, and per-class performance
Model | Validation | Test | Peak RAM | Latency | Deployed
Baseline — float32 (#1, original) | 88.8% | 74.5% | 14.6 KB | 250 ms | No
Compressed — int8 (#2, 250 ms) | 74.1% | 54.8% | 7.6 KB | 60 ms | No
Final — int8 on-device (#3, EON) | 91.6% | 79.4% | 11.8 KB | 127 ms | Yes
Three iterations: baseline 500 ms (#1), a lighter 250 ms variant (#2, lowest RAM & latency but accuracy fell), and the final 500 ms model (#3) chosen for best test accuracy. Final flash 75.9 KB; all test numbers at the 0.5 confidence threshold.
PER-CLASS TEST ACCURACY — final model (0.5 confidence threshold)
Chart: 
| Good | Ground | Top
Accuracy | 94.9 | 90.9 | 60.3
0.93
Area under ROC
(weighted)
The final model lifts Top from 48% to 60%; Good & Ground stay strong. Top still overlaps with Good — the remaining ceiling.
Notes: Results. Three iterations: baseline (#1, 74.5% test), a lighter 250 ms compressed variant (#2, smallest but accuracy fell to 54.8%), and the final model (#3) at 79.4% test, AUC 0.93. The final fixed most of the Top problem, 48% up to 60%. Stress these are all held-out test numbers at the same 0.5 threshold.

## Slide 9
On-Device Deployment Evidence
Live inference on the Arduino Nano 33 BLE Sense
Live on-device inference — good / ground / top
DEPLOYED MODEL
Impulse #3 — int8, EON-compiled
microphone_continuous sketch
Serial Monitor @ 115200 baud
Prints predicted class + confidence for each 500 ms window
~12 KB tensor arena (activations)
127 ms
inference latency / window
11.8 KB
peak RAM (tensor arena)
75.9 KB
Flash footprint
int8
quantized, EON-compiled
Notes: Demo evidence. Show the Serial Monitor screenshot / board. State latency, RAM, flash. This is also your live demo - run a few swings if doing it live.

## Slide 10
Key Challenges & Solutions
What broke, and how we fixed it
Short, variable-length impact clips
500 ms window with zero-padding to fit every swing
Validation-to-test generalization gap
Augmented data in the training set only — no leakage
Aggressive aug. mangled Top transients
Switched to gentle shift + light-noise augmentation
Many low-confidence “uncertain” calls
Tuned confidence threshold 0.6 → 0.5
MFE autotune degraded separation
Reverted to default DSP parameters
Top / Good acoustic overlap
Identified as a data ceiling → collect more real Top swings
Notes: Challenges. Pick two or three to narrate; do not read all six. The leakage-aware split and the augmentation fix are the strongest stories.

## Slide 11
Conclusion & Takeaways
WHAT WORKED
Final model: 79.4% test accuracy, AUC 0.93
Good (95%) and Ground (91%) strong; Top lifted to 60%
Runs on-device: 11.8 KB RAM, 75.9 KB Flash, 127 ms
WHAT WE LEARNED
Augmentation must respect signal characteristics
Honest, leakage-free testing reveals the real number
Auto-optimization (EON autotune) isn’t always better
NEXT STEPS
Record more real Top swings to break the Top–Good ceiling
Stream results over BLE to a phone for live feedback
Add more swing classes (slice, shank, sweet-spot)
Explore on-device fine-tuning per golfer
Notes: Conclusion. What worked, what we learned, what is next. End on BLE-to-phone as the natural extension.

## Slide 12
References & Tools
Datasets, tools, and platforms used
Edge Impulse Studio
Data pipeline, MFE DSP, model training, int8 quantization, EON Compiler, Arduino library export
TensorFlow Lite for Microcontrollers
On-device int8 inference runtime
Arduino Nano 33 BLE Sense
Target hardware — Cortex-M4F @ 64 MHz, onboard PDM microphone
Dataset
Self-collected golf-swing audio (Good / Ground / Top), augmented with a custom Python pipeline
Project
Edge Impulse public project — studio.edgeimpulse.com/public/1027938/live
Notes: References. Leave up briefly; mention the public Edge Impulse project link is live for graders.